## Slide 2: TEAM DETAILS AND PROBLEM STATEMENT
PROJECT TITLE : Smart Energy meter and power theft detection
TEAM NAME : INNOVATERS ARONA
Team members : Hemesh Gaur , Harsh Katara , Harshita Gochar , Doli Kanwar Rajawat
Problem :
Regional Issues & Detection Gaps
High-Loss States: States like UP, Bihar, Jharkhand, and Rajasthan report losses exceeding 25% to 35%.
Common Theft Methods: Direct hooking (katiyabaazi ), meter bypassing, slow-speed tampering, and faulty equipment.
No Real-Time Tracking: Lack of automated instant alerts leads to heavy transformer overloads and fire hazards.
Massive Financial & Transmission Losses
National Loss: ~15% to 23% of total generated electricity goes into transmission, distribution, and commercial losses (AT&C losses > 25% in several states).
Economic Burden: Power theft and commercial leaks cost utilities over ₹30,000 to ₹50,000 crores annually, with total AT&C losses exceeding ₹1 Lakh Crore.

## Slide 3: SOLUTION
Automated Tamper Logic
Compares line vs. neutral current differences and detects physical cabinet breaches instantly.
Cloud Dashboard & Cutoff
Pushes instant alerts to utility servers and enables automated relay power cutoff for defaulting nodes.
Smart IoT Hardware
Microcontroller-based energy monitoring unit continuously measuring real-time voltage, current, and active power.
Data Acquisition
Edge Processing
Cloud Transmission
Automated Action
Telemetry data transmitted securely via Wi-Fi / MQTT protocol .
Instant alert triggered on cloud dashboard for field audits and cutoff .
ESP 32 computes consumption parameters and analyses anomalies locally .
Sensors measure voltage , current , and power factor continuously .

## Slide 4: TECHNICAL APPROCH AND COMPONENT USED
Hardware Stack
Microcontroller: ESP32 / Node MCU Wi-Fi Module
Current , Voltage & power: PZEM-004T Module
Tamper Security: Limit switches & magnetic sensors
Actuator: 5V Relay module for automated cutoff
Software & Cloud
Firmware: Embedded C++ (Arduino IDE)
Backend/Cloud: Firebase Realtime DB / Node-RED
Frontend UI: HTML5, CSS3, JavaScript Web Dashboard
Communication Protocol: MQTT / HTTP REST APIs

## Slide 5: INNOVATION AND FEASIBILITY
Unique Selling Point (USP)
Dual-layer detection (bypass + physical cabinet breach).
Under 3-second rapid response notification latency.
Affordable retrofit design compatible with existing infrastructure .
Socio-Economic Feasibility
Recovers billions in lost revenue for power distribution networks .
Reduces technical carbon footprints via optimized grid loads.
High scalability potential for municipal smart grids

## Slide 6: CONCLUSION
Future Scope & Scalability
Conclusion
Financial Recovery: Provides a robust, automated defense mechanism against India's massive ₹30,000–₹50,000 Crore annual commercial power losses.
Operational Efficiency: Eliminates manual inspection delays by combining real-time IoT metrics with edge-computed anomaly triggers.
Smart Grid Integration: Seamless scaling with national smart metering infrastructure and centralized SCADA dispatch systems.
AI Predictive Maintenance: Expanding local micro-ML models to predict transformer overloads before physical failure occurs.
Renewable Energy Extension: Adapting differential energy auditing algorithms to track rooftop solar feed-ins and micro-grid theft patterns.

## Slide 7: THANKYOU !